## Slide 1: Application of electrodes to facilitate biological redox reactions in bioremediation and wastewater treatment: The novel technology of MICROBIAL FUEL CELLS
by Roald Kommedal

## Slide 2: Application of electrodes to facilitate biological redox reactions in bioremediation and wastewater treatment
Cell-
biology
Redox-
reactions
Bio-
films
Electro-
chemistry
What is this?

## Slide 3: Redox reactions
Redox reactions (Reduction/Oxidation reactions) are chemical reactions where electron(s) are transfered from one compound (the electron donor) that’s being oxidised, to a second compound (the electron acceptor) that is being reduced. The mechanism of electron transfer may be:
By direct (or close) contact between the donor and the acceptor
By transfer of the electrons by conducting materials (conductors)
By chemical compounds called electron carriers

## Slide 4: Biological redox reactions
Carbon
Macro and
micro-
nutrients
External
C-
source
Internal
C-source
from e-
donor
2 NAD+
2 NADH
ADP
ATP
Energy
½ O2
H2O
Electron
acceptor
C6H12O6
Electron donor
Energy synthesis
Cell mass
ATP
ADP
Cell
Synthesis
CO2

## Slide 5: Electrochemical cell
Oxidation at the anode:
H2 (g)  2 H+ + 2 e-
Reduction at the cathode:
Cu2+ + 2 e-  Cu (s)
Standard redox potentials
At 0 A (i.e. no electron flow) the potential is 0.334 V  EMF
Overall:
Cu2+ + H2 (g)  Cu (s) + 2 H+
If EMF > 0  Forward Spontaneous
EMF < 0  Reverse spontaneous

## Slide 6: Example: The Fuel Cell
At the anode (oxidating reaction):
H2 (g)  2 H+ + 2 e- E0 = 0.00V (def.)
At the cathode (reducing reaction):
½ O2 (g) + 2 H+ + 2 e-  H2O E0 = 1.229 V
Overall:
H2 (g) + ½ O2 (g)  H2O
E0tot = E0cathode – E0anode = 1.229 V – 0 V
Spontaneous (at standard conditions)
The reverese is non spontaneous
Can we force the reverse reaction to occur?

## Slide 7: Reversability: Electrolysis
By applying a potential that is higher than E0tot (same polarity) we may force electrons the other direction, so that a reduction occur at the former anode (now cathode), and an oxidation occur at the former cathode (now anode).
The overall reaction has simply been reversed.
H2O  H2 (g) + ½ O2 (g)
E0tot = E0cathode – E0anode + E =
0 V – 1.229 V + 1.3 V
Spontaneous (at standard conditions)
Two important relations:

## Slide 8: Bacteria growing on surfaces: Biofilms
A biofilm consists of cells immobilized at a substratum and frequently embedded in an organic matrix of microbial origin
(Characklis, 1990)

## Slide 9
Redox zonation due to diffusive transport

## Slide 10: The pieces have been laid....
Metabolism: Generation of energy by transfer of electrons through microbial cells
Redox reactions: Chemical reactions that release and accept electrons
Electrochemical cell: Separation of the redox half reactions, and transfer of electrons by external conductor
Biofilms: Living cells growing ON a surface
Let us bring them together....

## Slide 11: Two ways of combining electrochemical cells and microorganisms:
By spontaneous reactions : The Bio-Electrochemical Cell (The bio-fuel cell)
By non-spontaneous reactions: The Bio-Electrochemical Reactor (The bio-electrolytic cell)

## Slide 12: The ”Bio-Electrochemical cell” (summerised by: Wingard Jr., L.B., Shaw, C.H. and Castner, J.F. (1982) The bioelectrochemical cell, Enz. Microb. Technol., 4, pp. 137-142)
Application of biofilms to catalyse the oxidation of electron donors at the anaerobic anode of fuel cells. Using microorganisms as anode catalysts open up for numerous, especially organic, electron donors, and permit operations at significantly higher power outputs.
C6H12O6 + 6 H2O  6 CO2 + 24 H+ + 24 e-
6 O2 (g) + 24 H+ + 24 e-  12 H2O
C6H12O6 + H2O
NADH
NAD+
ADP
ATP
Growth
CO2
e-
H+
C6H12O6
24 H+
6 CO2
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-

## Slide 13: Possibilities and limitations
Microorganisms or cell free enzymes as catalysts
Some species synthesize extracellular electron shuttling compounds (some Clostridium, Shewanella and Geothrix sp.)
Direct electric energy production from wastewater
Most organisms do not carry out complete oxidation
Toxic intermediate formation inside biofilm
Need for external electron carriers, or mediators, that are a) toxic, b) degradable, a) may not be used in open environments
Consuming buffer

## Slide 14: Direct electron transfer
Electric energy may be harvested directly from marine sediments (however, 10 mW/m2; electrode surface) (Reimers, C.E., Tender, L.M, Fertig, S. and Wang, W. (2001) Env. Sci. TEch., 35, pp. 192-195
Geobacteraceae were higly enriched at the anode
Desulfuromonas acetoxidans (a Geobacteraceae) were found to deliver electrons directly to the anode (Bond, D.R:, Holmes, D.E., Tender, L.M. and Lovely, D.R. (2002), Science, 295, pp. 483-485)
The same autors also found that Geobacter metallireducens oxidised aromatic compounds (Benzoate and Toluene) in a three electrode system
Geobacter sulfurreducens delivered electrons directly to the anode during acetate oxidation at 0.2 V (13 mW/m2) (Bond, D.R. and Lovely, D.R. (2003) Appl. Env. Microbiol. 69, pp. 1648-1555)
Rhodoferax ferrireducens is able to oxidise Glucose by direct electron transfer without mediators (Chaudhuri, S.K. and Lovley, D.R. (2003) Nature Biotech., 21, pp. 1229-1232)

## Slide 15: Bond and Lovely (2003)
5 mM Acetate initially
Monolayer biofilm
No mediators
No suspended culture
Growth control by nutrients
97% electron recovery during non-growth
Potentiostat (0.2 V) power output concentration dependant (2  10 mM gave 0.03  0.23 W/m2)
Stable for more than 4 weeks
Large internal (electrolyte) potential drop (E = 0.99 V)
Similar results obtained for H2
e- transfer mechanism unknown

## Slide 16: Application: Oxidation of reduced compounds
Combinations of electrodes and biologically catalysed redox reactions may be used to produce electric energy from liquids containing reduced organic compounds.
Wastewater (on the average: C18H19O9N) contain abundant reduced compounds we normally spend a lot of energy on in order to oxidise ...

## Slide 17: The Bio-Electrolytic cell
The electron flow may be reversed by applying a higher potential than E between the electrodes.
This technique has seen many applications in industrial wastewater treatment were strong oxidants (Cl2, ClO2, HOCl, O3, H2O2, and OH* ) are generated at the anode. However, non-toxic molecular O2 may also be generated by low potentials.
At the cathode electron acceptors are reduced, and these may be used to promote microbial growth.

## Slide 18: Bio-Electrochemical Reactors
electron acceptor
H+
CO2
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
H2
H2 + CO2
NADH
NAD+
ADP
ATP
Growth
Reduced electron acceptor

## Slide 19: Applications in:
Bioremediation
  Electron donor and acceptor introduction
  In situ nitrate removal
  Nutrient supply
  Controlled electron donor or acceptor migration
  Electric soil heating coupled with vapor extraction
Wastewater tratment
  Autotrophic denitrification
  Simultaneous nitrification/denitrification (N-removal)
  Organic matter reduction (with energy production)

## Slide 20: Bio-electrochemical denitrification (Sakakibara, Y. and Kuroda, M. (1993) Biotech. Bioeng., 42, pp. 535-537)
H2
NADH
NAD+
ADP
ATP
H2O + N2
NO3-
H+
CO2
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
H2
NO3-
5 H2 (g) + 2 NO3- + 2 H+  N2 + 6 H2O
10 H+ + 10 e-  5 H2 (g)
2½ C + 5 H2O  2½ CO2 (g) + 10 H+ + 10 e-

## Slide 21
Heterotrophic H2 driven denitrification
Electrolysis was rate limiting
100 % electron efficiency
Carbon oxidation at the anode
Power requirement: 16.5 W/g NO3- oxidised
Results:
Overall reaction: 2 NO3- + 2 H+ + 2½ C  N2 + 2 ½ CO2 + H2O
No oxygen developed (C-oxidation at the anode)
CO2 buffer the alkaline denitrification (pH stabilisation)
Biofilm prevent H2 diffusion into solution (no permeable membrane required)

## Slide 22
Sakakibara, Y., Araki, K., Tanaka, T., Watanabe, T. and Kuroda, M. (1994) Denitrification and neutralisation with an electrochemical and biological reactor, Wat. Sci. Tech., 30, pp. 151-155
Sakakibara, Y., Flora, J.R., Suidan, M.T. and Kuroda, M. (1994) Modelling of electrocj\hemical-activated denitrifying biofilms, Wat. Res., 28, pp. 1077-86
Simultaneous oxidation and reduction treatment of polluted water by a bio-electro reactor, Wat. Sci. Tech., 34, pp. 101-108
Sakakibara, Y., Araki, K., Watanabe, T. and Kuroda, M. (1997) The denitrification and neutralisation perfomance of an electro-chemically activated biofilm reactor used to treat nitrate contaminated groundwater, Wat. Sci. Tech., 36, pp. 61-68
Kuroda, M., Watanabe, T. and Umedu, Y. (1997) Simultaneous COD removal and denitrification of wastewater by bio-electrode reactors, Wat. Sci.Tech., 8, pp. 161-168
Cast, K.L. and Flora, J.R.V. (1998) An evaluation of two cathode materials and the impact of copper pn bioelectrochemical denitrification, Wat. Res., 32, pp. 63-70
Feleke, Z., Araki, K., Sakakibara, Y., Watanabe, T. and Kuroda, M. (1998) Selective reduction of nitrate to nitrogen gas in a biofilm-electrode reactor, Wat. Res., 32, pp. 2728-34
Islam, S. and Suidan, M.T. (1998) Electrolytic denitrification: Long term perfomance and effect of current intensity, Wat. Res., 32, pp. 528-36
Sakakibara Y. and Nakayama T. (2001) A novel multielectrode system for electrolytic and biological water treatments: Electric charge transfer and applications to denitrification, Wat. Res., 35, pp. 768-78
Combined bioelectrochemical and sulfur autotrophic denitrification for drinking water treatment, Wat. Res., 37, pp. 3767-75
Alg. immob.denitrifiers; stainless steel cathode; CO2 evolution demonstrated, =2.2 V  22 W/g NO3- rem
Net denitr. rate depends show ”bell shaped” relation to the electrode current
Simultaneous nitrification/ denitrification; enhanced denitr. at C/N 1
Continuous denitr. of artificial groundwater incl. DO, SO42- and no buffer; no SO42- reduction observed
H2 driven denitr. at high organic COD levels
Stainless steel and graphite electrodes are similar; Cu electrodes inhibit denitr.
Long periode (>12 months) denitr. of surface and groundwater; no effects of competing anions.
Cont. long term denitr. of 0.8 g N/m2.d (20 mg/l); 98% rem.at 20 mA
Increased cathode area; HCO3- mediated charge transfer
Electrochemical autotrophic denitr. post treatment following sulfur oxidation

## Slide 23: High rate bio-electrochemical denitrification (Prosnansky, M., Sakakibara, Y. and Kuroda, M. (2002) Wat. Res., 36, pp. 4801-10
High rate: 3.1 g N/m2.d
90% NO3- reduction (< 5 mg/l)
HRT = 1.5-3 h
40-60 W/g NO3- removed (including DO removal; 5 mg/l in)
Cost estimation
  46 øre/kWh (NOR)
  500 øre/kg CO2 (JAP)
  Operational costs: 10 øre/g Nrem
  Tot. costs (103 m3/d): 30-35 øre/g Nrem
Ion Exch. and RO: 20 and 60 øre/g Nrem
Higher rates: Increase cathode area by electrically connected GAC (63 m2/m3)
Introduce CO2 as buffer, C-source and electrolyte
Flow through design (cont. plug flow) with post-aerobic stabilisation
Inert electrodes (Pt and SS)

## Slide 24: Bioremediation: Denitrification of groundwater
Aquifers contaminated by agricultural runoff (fertilisers).
NO3- drinking water standards (WHO): 10 mg/l, NO2- < 0.1 mg/l
Standard technique: Denitrification by added electron donor
Residual electron donor must be kept low to prevent heterotrophic growth
Autotrophic denitrification has promising features:
5 H2 + 2 NO3-  N2 + 4 H2O + 2 OH-
  Low biomass yield
  Low residual e-donor
  Low water solubility
  May be produced by electrolysis

## Slide 25: Indirect facilitation of biological redox reactions
Direct migration of in situ ions to be removed (e.g. heavy metals) to electrodes for enhanced bioreduction
Transport of ionised nutrients to low permeability aquifers
DC
Nutrients (anions)
Nutrients (cations)
-
+
Low permeable zone
Higher permeability
Higher permeability
DC
Nutrients
Nutrients
-
+
Cations
Anions

## Slide 26: Summary ...
The bioelectrochemical cell
  Remove electron donors by a spontaneous reaction
  Remove electron acceptors by spontaneous reaction
The bioelectrolytic cell
  Remove electron donors by electrolysis
  Remove electron acceptors by electrolysis
in both applications:
Electrodes facilitates biological redox reactions by separation of half reactions
Microorganisms facilitate the redox reactions as catalysts

## Slide 27: Speculations on other applications...
Oxygenation without stripping
  H2S removal
  Odour removal
Microaerophilic biogas production
Simultaneous nitrification/denitrification
Removal of electron acceptors from injection water combined with produced water oxidation

## Slide 28: Some last minute progressionism...
May represent a significant energy source
Combined energy production and bioremediation
Easy and gentle way of introducing electron donors and acceptors
Combination of half-reactions may improve bioreactor perfomance and design
Combination of biological and chemical oxidation technologies

## Slide 29: ... and some last minute scepticism.
Electron consuming side reactions
Potential of producing strong oxidants
Unwanted side reaction products in complex media
Difficult to control (especially in bioremediation)
Need to bring this out of the lab!! Pilot and full scale experience